## Slide 1
Exercise 10 · Digital Biomarker
1/3
Scientific question
Smartphone motion sensors as a proof‑of‑concept digital biomarker for gait stability
Can accelerometer and gyroscope signals distinguish normal walking from unstable walking?
Hypothesis: unstable walking causes more irregular and abrupt motion patterns.
Medical relevance: gait instability can be a signal for fall risk, balance problems, medication side effects, fatigue, or disease progression.
Experiment 1: normal walking
Experiment 2: unstable walking
1
participant
2
conditions
2
phone sensors
8.88s
matched analysis window
Sensors
Accelerometer
Gyroscope
Cleaning
split gaps
trim duration
resample 50 Hz
Features
variability
jerk
peak intervals
Answer
Compare digital biomarkers between walking conditions
Study design
Two short walking recordings were analyzed from the uploaded sensor JSON. Because the raw timestamps included a gap in experiment 1, the analysis uses continuous segments and relative sensor time instead of raw wall-clock duration.
Notes: Slide 1 introduces the scientific question and the experimental setup. Emphasize that this is a proof of concept rather than clinical validation.

## Slide 2
Exercise 10 · Digital Biomarker
2/3
Sensors and preprocessing
The raw normal-walking recording contained a large gap; the analysis uses only clean continuous segments
Cleaning decision
A gap > 1 second starts a new segment. For each experiment, the longest usable continuous segment is selected.
12.37s
normal clean segment
8.88s
unstable clean segment
≈51.5 Hz
accelerometer rate
50 Hz
resampled analysis
Sensors used
Primary: LSM6DSO Accelerometer for movement intensity, peak timing and jerk. Supporting: LSM6DSO Gyroscope for rotational instability.
Final comparison: both conditions are trimmed to the shared 8.88‑second window, so the feature values describe comparable time spans.
Notes: Slide 2 explains why the normal walking sampling rate looked wrong. The raw duration was affected by a 56.7-second gap. After segment detection, both accelerometer rates are roughly 51 Hz.

## Slide 3
Exercise 10 · Digital Biomarker
3/3
Analytics and results
Features are extracted from cleaned, aligned and resampled accelerometer signals
Key results from the notebook
0.37 vs 0.18
peak interval CV unstable vs normal
+48%
acceleration range
+11%
dynamic RMS
+4%
mean absolute jerk
Interpretation
Unstable walking shows more irregular peak timing and larger movement spikes. This supports the idea that phone motion sensors can capture gait instability as a digital biomarker.
Limitation: one participant and short trials, so this is a proof of concept, not clinical validation.
Notes: Slide 3 should be presented as the analytics answer. Explain the pipeline: magnitude calculation, baseline removal, feature extraction and feature comparison. The strongest result is peak interval variability, roughly doubled in unstable walking.